## Slide 1: Exploring Environmental Science for AP®
1st Edition
Chapter 14
Nonrenewable Energy
Copyright © 2018 Cengage Learning. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Core Case Study: Using Hydrofracking to Produce Oil and Natural Gas (1 of 2)
Oil and natural gas trapped between compressed layers of shale rock formations
New technologies allowed access
  Horizontal drilling
  Hydraulic fracturing (hydrofracking)
    Pump water, sand, and chemicals into cracks
    Produces hazardous waste slurry

## Slide 3: Core Case Study: Using Hydrofracking to Produce Oil and Natural Gas (2 of 2)
Notes: Figure 15.1 Fracking: Horizontal drilling and hydraulic fracturing are used to release large amounts of oil and natural gas that are tightly held in underground shale rock formations.

## Slide 4: 14.1 What Types of Energy Resources Do We Use?
90% of the commercial energy used in the world comes from nonrenewable resources
  Oil, natural gas, and coal
Energy resources vary greatly in their net energy
  Amount of energy available from a resource minus the amount of energy needed to make it available

## Slide 5: Where Does the Energy We Use Come From? (1 of 2)
Energy that heats the earth comes from the sun
Commercial energy is sold in the marketplace
  Nonrenewable
    Oil, coal, natural gas, and nuclear energy
  Renewable
    Solar, hydropower, biomass, geothermal, and wind

## Slide 6: Where Does the Energy We Use Come From? (2 of 2)
Notes: Figure 15.2 Energy use by source throughout the world (left) and in the United States (right) in 2014.

## Slide 7: Net Energy: It Takes Energy to Get Energy (1 of 3)
Each step in making energy available uses high-quality energy
  Example: oil must be found, pumped, transferred to a refinery, converted to gasoline, and delivered to consumers
Net energy yield
  Amount of high-quality energy available from a resource minus the high-quality energy needed to make the energy available

## Slide 8: Net Energy: It Takes Energy to Get Energy (2 of 3)
Net energy ratio
  Also called energy returned on investment
  Energy obtained per unit energy used to obtain it
Energy efficiency
  Getting more useful work using less energy; heating buildings, producing electricity, driving more efficient cars

## Slide 9: Net Energy: It Takes Energy to Get Energy (3 of 3)
Notes: Figure 15.3 Generalized net energies for various energy resources and systems (Concept 15.1). Critical thinking: Based only on these data, which two resources in each category should we be using?

## Slide 10: 14.2 What Are the Advantages and Disadvantages of Using Oil?
Conventional crude oil is abundant
  Medium net energy yield
  Causes air and water pollution
  Releases CO2 into the atmosphere
Unconventional heavy oil from oil shale rock and oil sands
  Potentially large supplies
  Low net energy yield
  Higher environmental impact

## Slide 11: We Depend Heavily on Oil (1 of 3)
Crude oil (petroleum)
  Contains combustible hydrocarbons
Peak production
  Time after which production from a well declines
Crude oil cannot be used as it comes out of the ground
  Must be refined using high-quality energy
  Petrochemicals–byproducts

## Slide 12: We Depend Heavily on Oil (2 of 3)
Notes: Figure 15.4a When crude oil is refined, many of its components are removed at various levels of a distillation column, depending on their boiling points. The most volatile components with the lowest boiling points are removed at the top of the column, which can be as tall as a nine-story building.

## Slide 13: We Depend Heavily on Oil (3 of 3)
Notes: Figure 15.4b The photo shows an oil refinery in Texas.

## Slide 14: Is the World Running Out of Crude Oil? States (1 of 2)
Proven oil reserves–available deposits
  12 OPEC countries have 81% of the world’s proven crude oil reserves
    These countries play a role in regulating global prices by agreeing to increase or decrease the amount produced
Increasing shortage of cheap oil
  Easy-to-reach deposits are quickly being depleted

## Slide 15: Case Study: Oil Production and Consumption in the United States (1 of 3)
Notes: Figure 15.5 Countries with the largest proven crude oil reserves, oil production, and oil consumption in 2014

## Slide 16: Case Study: Oil Production and Consumption in the United States States (2 of 3)
U.S. commercial energy sources
  82% from fossil fuels
    Largest portion comes from crude oil
U.S. oil consumption exceeds domestic production
  Must import oil
Recent rise in domestic production of tight oil from shale rock
  Likely to peak around 2020 and then decline

## Slide 17: Case Study: Oil Production and Consumption in the United States (3 of 3)
Notes: Figure 15.6 Using conventional light oil as an energy resource has advantages and disadvantages. Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do the advantages of relying on conventional light oil outweigh its disadvantages? Explain.

## Slide 18: Use of Heavy Oil Has a High Environmental Impact (1 of 5)
Shale oil
  Oil that is integrated within bodies of shale rock
    As opposed to being trapped between layers of rock
  Production involves mining, crushing, and heating the rock
    Extracts kerogen that can be distilled

## Slide 19: Use of Heavy Oil Has a High Environmental Impact (2 of 5)
Notes: Figure 15.7 Heavy shale oil (right) can be extracted from oil shale rock (left).

## Slide 20: Use of Heavy Oil Has a High Environmental Impact (3 of 5)
Oil sands (tar sands) another source of heavy oil
  Contains bitumen
  Extensive deposits in Canada
Extraction
  Clear-cutting forests and strip-mining the land
  Low net energy yield
  Requires much water
  Emits pollutants

## Slide 21: Use of Heavy Oil Has a High Environmental Impact (4 of 5)
Notes: Figure 15.8 Oil sands surface mining operation in Alberta, Canada, involves clearing boreal forest and strip-mining the land to remove the oil sands.

## Slide 22: Use of Heavy Oil Has a High Environmental Impact (5 of 5)
Notes: Figure 15.9 Using heavy oil from oil sands as an energy resource has advantages and disadvantages (Concept 15.2). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do the advantages of relying on heavy oil from oil sands outweigh its disadvantages? Explain.

## Slide 23: 14.3 What Are the Advantages and Disadvantages of Using Natural Gas?
Natural gas
  Mostly methane
    Propane, butane, and hydrogen sulfide in smaller amounts
  Has a medium net energy yield and a fairly low production cost
  Burns cleaner than oil and coal
  Extracted through horizontal drilling and fracking

## Slide 24: Natural Gas Is a Versatile and Widely Used Fuel (1 of 2 )
Liquefied petroleum gas (LPG)
  Stored in pressurized tanks for use in rural areas
Liquefied natural gas (LNG)
  Can be transported across oceans
  Low net energy yield
  The United States currently exports to other nations

## Slide 25: Natural Gas Is a Versatile and Widely Used Fuel (2 of 2 )
Notes: Figure 15.11 Using conventional natural gas as an energy resource has advantages and disadvantages. Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using conventional natural gas outweigh its disadvantages? Explain.

## Slide 26: Science Focus 14.1: Environmental Effects of Natural Gas Production and Fracking in the U.S. (1 of 2)
Fracking has several harmful environmental effects
  Requires enormous volumes of water
  Produces hazardous wastewater
    Earthquakes could release into groundwater
  Failure of well-casing cement causes contaminated ground water
Natural gas fracking excluded from EPA regulations in 2005

## Slide 27: Science Focus 14.1: Environmental Effects of Natural Gas Production and Fracking in the U.S. (2 of 2)
Notes: Figure 15.A Natural gas fizzing from this faucet in a Pennsylvania home can be lit like a natural gas stove burner. This began happening after an energy company drilled a fracking well in the area, but the company denies responsibility. The homeowners have to keep their windows open year-round to keep the lethal and explosive gas from building up in the house.

## Slide 28: Can Natural Gas Help to Slow Climate Change?
Emits less CO2 per unit of energy than coal
Low price could slow shift to other renewable energy resources
Methane a much more potent greenhouse gas than CO2
  Drilling, production, and distribution of natural gas releases large quantities of methane

## Slide 29: 14.4 What Are the Advantages and Disadvantages of Coal? (1 of 2)
Conventional coal is plentiful
  High net energy yield
  Low cost
  Using it has a high environmental impact
We can produce gaseous and liquid fuels from coal
  Lower net energy yields
  Higher environmental impacts than conventional coal

## Slide 30: 14.4 What Are the Advantages and Disadvantages of Coal? (2 of 2)
Notes: Figure 15.18 Using coal as an energy resource has advantages and disadvantages. Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using coal as an energy resource outweigh its disadvantages? Explain.

## Slide 31: Coal Is a Plentiful but Dirty Fuel (1 of 4)
Coal
  Solid fossil fuel formed from remains of land plants
Burned in power plants
  Generated 40% of the world’s electricity in 2015
Largest consumers of coal
  China, the United States, and India

## Slide 32: Coal Is a Plentiful but Dirty Fuel (2 of 4)
Environmental costs of burning coal
  Mining coal severely degrades land
  Water and air pollution
    Soot and CO2
    Trace amounts of mercury and radioactive materials
  Scrubbers remove some pollutants before they leave smokestacks
    Produces coal ash that must be safely stored

## Slide 33: Coal Is a Plentiful but Dirty Fuel (3 of 4)
Notes: Figure 15.12 Over millions of years, several different types of coal have formed. Peat is a soil material made of moist, partially decomposed organic matter, similar to coal; it is not classified as a coal, although it is used as a fuel. These different major types of coal vary in the amounts of heat, carbon dioxide, and sulfur dioxide released per unit of mass when they are burned.

## Slide 34: Coal Is a Plentiful but Dirty Fuel (4 of 4)
Notes: Figure 15.17 CO2 emissions, expressed as percentages of emissions released by burning coal directly, vary with different energy resources. Data analysis: Which of these produces more CO2 emissions per kilogram: burning coal to heat a house, or heating with electricity generated by coal?

## Slide 35: We Are Not Paying the Full Cost of Using Coal
Harmful environmental and health costs
  Not included in market price of coal-generated electricity
Ways to implement full-cost pricing
  Phase out subsidies and tax breaks
  Require stricter air pollution controls
  Tax CO2 emissions
  Regulate coal ash as a hazardous waste

## Slide 36: The Future of Coal
U.S. coal use dropped 18% between 2007 and 2013
  Increased competition from natural gas, wind, and solar power
  Grassroots political opposition
Natural gas should overtake coal as largest electricity source by the 2030s
U.S. coal producers are exporting coal
  Use is expanding in India, Africa, and Asia

## Slide 37: We Can Convert Coal into Gaseous and Liquid Fuels (1 of 2)
Conversion of solid coal to synfuels
  Synthetic natural gas (SNG) by coal gasification
  Methanol or synthetic gasoline by coal liquefaction
Producing synfuels requires mining of 50% more coal
  Lower net energy and cost more to produce than coal

## Slide 38: We Can Convert Coal into Gaseous and Liquid Fuels (2 of 2)
Notes: Figure 15.19 The use of synthetic natural gas (SNG) and liquid synfuels produced from coal as energy resources has advantages and disadvantages (Concept 15.2). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using synfuels produced from coal as an energy source outweigh its disadvantages? Explain.

## Slide 39: 14.5 What Are the Advantages and Disadvantages of Using Nuclear Power?
Nuclear power has a low environmental impact and a very low accident risk
Drawbacks
  Low net energy yield
  High costs
  Fear of accidents
  Long-lived radioactive wastes
  Role in spread of nuclear weapons technology

## Slide 40: How Does a Nuclear Fission Reactor Work? (1 of 4)
Controlled nuclear fission reaction in a reactor
  Light-water reactors
  Boil water to produce steam to spin a turbine
  Fueled by uranium ore mined from the earth’s crust
    Enriched uranium packed as pellets in fuel rods and fuel assemblies
  Control rods absorb neutrons

## Slide 41: How Does a Nuclear Fission Reactor Work? (2 of 4)
Water is the usual coolant
Containment shell around the core for protection
Emergency core cooling system
Typical cost to construct
  $9–11 billion
United States, France, and Russia
  Leading producers of nuclear power in 2014
Notes: 41

## Slide 42: How Does a Nuclear Fission Reactor Work? (3 of 4)
Notes: Figure 15.20 Nuclear fission is the source of energy for producing electricity in a nuclear power plant.

## Slide 43: How Does a Nuclear Fission Reactor Work? (4 of 4)
Notes: Figure 15.21 Nuclear power plant. Intense heat from the nuclear fission of uranium-235 in a chain reaction (Figure 15.20) in the core of this pressurized water-cooled nuclear power plant is transferred to two heat exchangers and converted to steam, which spins a turbine that generates electricity. About 65% of the energy released by the nuclear fission of the plant’s uranium fuel is wasted. It ends up as heat that flows into the atmosphere through gigantic cooling towers (shown in the photo) or into water from a nearby source that is used to cool the plant. Critical thinking: How does this plant differ from the coal-burning plant in Figure 15.13?

## Slide 44: What Is the Nuclear Fuel Cycle? (1 of 3)
Mining the uranium
Processing and enriching the uranium to make fuel
Using it in a reactor
Safely storing the radioactive waste
Retiring the worn-out plant
  Storing its high- and moderate-level radioactive parts safely

## Slide 45: What Is the Nuclear Fuel Cycle? (2 of 3)
Notes: Figure 15.22 Using nuclear power to produce electricity involves a sequence of steps and technologies that together are called the nuclear fuel cycle. Critical thinking: Do you think the market price of nuclear-generated electricity should include all the costs of the nuclear fuel cycle, in keeping with the full-cost pricing principle of sustainability? Explain

## Slide 46: What Is the Nuclear Fuel Cycle? (3 of 3)
Notes: Figure 15.23 Using the nuclear power fuel cycle (Figure 15.22) to produce electricity has advantages and disadvantages. Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using nuclear power outweigh its disadvantages? Explain.

## Slide 47: Dealing with Radioactive Nuclear Wastes (1 of 2)
Rods must be replaced every three to four years
Stored in water-filled pools for several years to cool
Transferred to dry casks
Can be processed to remove plutonium
  Reprocessing reduces storage time from 240,000 years to about 10,000 years
  Costly and produces weapons material

## Slide 48: Dealing with Radioactive Nuclear Wastes (2 of 2)
No permanent, secure repository exists today
  Nevada Yucca Mountain site plan abandoned
Retiring nuclear plants
  Enormous costs

## Slide 49: Can Nuclear Power Slow Climate Change?
Nuclear power plants–no CO2 emission
Nuclear fuel cycle–emits CO2
Cutting global CO2 emissions in half between 2015 and 2040 and meeting energy needs would require building 12,000 nuclear power reactors
  According to Mark Lynas, climate change author

## Slide 50: Controversy about the Future of Nuclear Power (1 of 3)
Nuclear reactors produced 19% of U.S. energy in 2014
67 new nuclear reactors under construction worldwide in 2015
U.S. government provides subsidies, tax breaks, and insurance for the nuclear industry
Accidents have dampened public confidence in nuclear power

## Slide 51: Controversy about the Future of Nuclear Power (2 of 3)
New technologies
  Advanced light-water reactors
    Built-in safety features
  Smaller, modular light water reactors
    Not yet built and evaluated
  Thorium-based reactors
    Less costly and safer

## Slide 52: Controversy about the Future of Nuclear Power (3 of 3)
Solutions
  Reactors must be built so that a runaway chain reaction is impossible.
  The reactor fuel and methods of fuel enrichment and fuel reprocessing must be such that they cannot be used to make nuclear weapons.
  Spent fuel and dismantled plants must be easy to dispose of without burdening future generations with harmful radioactive waste.
  Taking its entire fuel cycle into account, nuclear power must generate a net energy high enough so that it does not need government subsidies, tax breaks, or loan guarantees to compete in the open marketplace.
  Its entire fuel cycle must generate fewer greenhouse gas emissions than other energy alternatives.

## Slide 53: Case Study: The Fukushima Daiichi Nuclear Power Plant Accident in Japan
March 11, 2011 accident
  Triggered by major offshore earthquake and resulting tsunami
Important effects
  Increased fear about nuclear power
  Revealed single accident can cost $500 billion
  Some countries announced phasing out nuclear power
  Spurred Japan to reduce energy use

## Slide 54: Is Nuclear Fusion the Answer?
Fusion
  Two isotopes fused together to form a heavier nucleus
  Releases energy
  Technology used by the sun to release energy
Technology is very difficult to develop
  No approach has produced more energy than it has used

## Slide 55: Big Ideas (1 of 2)
Net energy
  Key factor in evaluating the long-term usefulness of any energy resource
Conventional oil, natural gas, and coal
  Plentiful with moderate to high net energy yields
  Use has a high environmental impact

## Slide 56: Big Ideas (2 of 2)
Nuclear power fuel cycle
  Low environmental impact
  Very low accident risk
  Downsides
    High costs
    Low net energy
    Long-lived radioactive wastes
    Role in spreading nuclear weapons technology

## Slide 57: Tying It All Together: Fracking, Nonrenewable Energy, and Sustainability
Horizontal drilling and fracking have greatly increased oil and natural gas production in the United States
Long-term usefulness of an energy resource depends on net energy
Challenge: find ways to reduce harmful environmental impacts of fossil fuels and nuclear energy
  Option: shift to renewable energy resources