## Slide 1: Exploring Environmental Science for AP®
1st Edition
Chapter 15
Energy Efficiency and Renewable Energy
Copyright © 2018 Cengage Learning. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Core Case Study: Saving Energy and Money and Reducing our Environmental Impact
About 43% of money Americans spend on energy is unnecessarily wasted
Sources of waste
  Inefficient use of gasoline in car engines
  Air leaks cause heat loss from buildings
Easy and cost-effective solutions
  Caulking home windows and doors
  Adding insulation

## Slide 3: 15.1 Why Do We Need a New Energy Transition?
World is in early stages of a transition
  Move from fossil fuels to energy efficiency and renewable energy

## Slide 4: Establishing New Energy Priorities
New energy transition is needed
  Improve energy efficiency and reduce energy waste
  Decrease dependence on nonrenewable fossil fuels
  Rely more on a mix of renewable energy sources
Benefits
  Save money, create jobs, reduce air pollution, keep climate change from accelerating
Shift due to
  increasing availability of cheaper solar and wind and advances in renewable technology

## Slide 5: Case Study: Germany Is a Renewable Energy Superpower
Germany’s 2050 goals
  Obtain 60% of energy from renewable resources
  Increase electricity efficiency by 50%
  Reduce CO2 emissions by 80–95%
  Sharply reduce use of coal
Feed-in-tariff
  Utilities must buy electricity from homeowners with solar cells and feed into electrical grid

## Slide 6: 15.2 Why Is Improving Energy Efficiency and Reducing Energy Waste an Important Energy Resource?
Improvements in energy efficiency and reductions in energy waste
  Could save at least one-third of the energy used in the world
    Up to 43% of energy used in the United States
Many technologies exist for increasing energy efficiency of industry, vehicles, appliances, and buildings

## Slide 7: We Waste a Lot of Energy and Money (1 of 4)
Energy efficiency
  How much useful work we get from each unit energy
Energy conservation
  Reducing or eliminating unnecessary energy waste

## Slide 8: We Waste a Lot of Energy and Money (2 of 4)
Some sources of waste
  Poorly insulated buildings
  Reliance on cars for getting around
  Huge data centers filled with electronic servers
    Use only 10% of energy they consume
  Motor vehicles with internal combustion engines
  Nuclear, coal, and natural gas power plants

## Slide 9: We Waste a Lot of Energy and Money (3 of 4)
Notes: Figure 16.2 Flow of commercial energy through the U.S. economy. Only 16% of the country’s high-quality energy ends up performing useful tasks. Critical thinking: What are two examples of unnecessary energy waste?

## Slide 10: We Waste a Lot of Energy and Money (4 of 4)
Notes: Figure 16.3 Improving energy efficiency and conserving energy has several benefits. Critical thinking: Which two of these benefits do you think are the most important? Why?

## Slide 11: Improving Energy Efficiency in Industries and Utilities
Cogeneration
  Combined heat and power
  Two forms of energy from same fuel source
Replace energy-wasting electric motors
Recycle materials
Use energy-efficient LED lighting
Meter energy use
Shut down unused computers and lights

## Slide 12: Building an Interactive and More Energy-Efficient Electrical Grid
Current electrical grid system–outdated and wasteful
Interactive grid
  Ultra-high-voltage
  Super-efficient transmission lines
  Digitally controlled
  Responds to local changes in demand and supply
  Easier to buy renewable energy
  Will save $2 trillion over next 20 years

## Slide 13: Making Transportation More Energy-Efficient
Hidden costs in gasoline
  Corporate Average Fuel Economy (CAFÉ)
  Government subsidies and tax breaks for oil companies
  All hidden costs add up to $12 per gallon
Build or expand mass transit and high speed rail
Carry more freight by rail instead of trucks
Encourage biking by building bike lanes

## Slide 14: Switching to Energy-Efficient Vehicles (1 of 2)
Gasoline-electric hybrid car
Plug-in hybrid electric vehicle
Electric vehicle with a hydrogen fuel cell
Car bodies made of light, composite materials

## Slide 15: Switching to Energy-Efficient Vehicles (2 of 2)
Notes: Figure 16.4 Solutions: A conventional gasoline–electric hybrid vehicle (left) is powered mostly by a small internal combustion engine with an assist from a strong battery. A plug-in hybrid electric vehicle (right) has a smaller internal combustion engine with a second and more powerful battery that can be plugged into a 110-volt or 220-volt outlet and recharged (see photo). An all-electric vehicle (not shown) runs completely on a rechargeable battery. Question: Would you buy one of these vehicles? Explain.

## Slide 16: Designing Buildings That Save Energy and Money (1 of 2)
Green architecture
Living or green roofs
  Specially formulated soil and vegetation
Superinsulation
  No need for heating system
U.S. Green Building Council’s Leadership in Energy and Environmental Design (LEED)
  Standards

## Slide 17: Designing Buildings That Save Energy and Money (2 of 2)
Notes: Figure 16.5 Green roof on Chicago’s City Hall.

## Slide 18: Saving Energy and Money in Existing Buildings (1 of 2)
Ways to reduce energy use
  Get a home energy audit
  Insulate the building and plug leaks
  Use energy-efficient windows
  Stop other heating and cooling losses
  Heat interior spaces more efficiently
  Heat water more efficiently
  Use energy-efficient appliances, computers, and lighting

## Slide 19: Saving Energy and Money in Existing Buildings (2 of 2)
Stepped Art
Notes: Figure 16.7 Individuals matter: You can save energy and money where you live and reduce your harmful environmental impact. Critical thinking: Which of these things do you already do? Which additional ones might you do?

## Slide 20: Why Are We Wasting So Much Energy and Money?
Energy remains artificially cheap
  Government subsidies
  Tax breaks
  Prices don’t include true cost
Few large and long-lasting incentives for improving energy efficiency and reducing waste
Rebound effect

## Slide 21: Relying More on Renewable Energy
Reasons renewable energy use is not more prevalent
  Inaccurate perceptions that solar and wind energy are unreliable and intermittent
  Government subsidies and tax breaks lower for renewable energy than for fossil fuels
  Prices for nonrenewable energy do not include harmful environmental impacts
  Energy shift takes many decades

## Slide 22: 15.3 What Are the Advantages and Disadvantages of Using Solar Energy?
Passive and active solar heating systems can heat water and buildings effectively
Cost of using sunlight to produce electricity is falling rapidly

## Slide 23: Heating Buildings and Water with Solar Energy (1 of 3)
Passive solar heating system
  Absorbs and stores heat from the sun directly within a well-insulated structure
Active solar heating system
  Captures energy from the sun in a heat-absorbing fluid

## Slide 24: Heating Buildings and Water with Solar Energy (2 of 3)
Notes: Figure 16.8 Solutions: Passive (left) and active (right) solar home heating systems.

## Slide 25: Heating Buildings and Water with Solar Energy (3 of 3)
Notes: Figure 16.10 Heating a house with passive or active solar energy system has advantages and disadvantages (Concept 16.3). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using these technologies outweigh their disadvantages?

## Slide 26: Cooling Buildings Naturally
Methods to keep a building cool
  Open windows when cooler outside
  Use fans
  Superinsulation and high-efficiency windows
  Shade trees, overhangs, or window awnings
  Light-colored roof
  Geothermal heat pumps bring cool air from underground

## Slide 27: Concentrating Sunlight to Produce High-Temperature Heat and Electricity (1 of 4)
Solar thermal systems
  Collect sunlight to boil water and produce steam to generate electricity
  Used in deserts and open areas with ample sunlight
  Require large volumes of cooling water for condensing steam and cleaning mirrors
Low net energy yields

## Slide 28: Concentrating Sunlight to Produce High-Temperature Heat and Electricity (2 of 4)
Notes: Figure 16.11 Solar thermal power: This solar power plant in California’s Mojave Desert uses curved (parabolic) solar collectors to concentrate solar energy to provide enough heat to boil water and produce steam for generating electricity.

## Slide 29: Concentrating Sunlight to Produce High-Temperature Heat and Electricity (3 of 4)
Notes: Figure 16.12 Solar thermal power: In this system in California an array of mirrors tracks the sun and focuses reflected sunlight on a central receiver to boil the water for producing electricity.

## Slide 30: Concentrating Sunlight to Produce High-Temperature Heat and Electricity (4 of 4)
Notes: Figure 16.13 Using solar energy to generate high-temperature heat and electricity has advantages and disadvantages (Concept 16.3). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using these technologies outweigh their disadvantages?

## Slide 31: Solar Cookers
Solar cookers can replace wood and charcoal fires
Notes: Figure 16.14 Solutions: Solar cooker (left) in Costa Rica and simple solar oven (right).

## Slide 32: Using Solar Cells to Produce Electricity (1 of 5)
Photovoltaic (PV) cells
  Convert solar energy to electric energy
Design of solar cells
  Sunlight hits cells and produces flow of electrons
  Systems can be connected to existing electrical grids or to batteries

## Slide 33: Using Solar Cells to Produce Electricity (2 of 5)
Solar cells made of paper-thin, rigid, or flexible sheets
  Enabled by nanotechnology and other emerging technologies
Rural use of solar
  Rooftop solar panels power LED lamps
  Solar powered microgrids

## Slide 34: Using Solar Cells to Produce Electricity (3 of 5)
Problem with current solar cells
  Low energy efficiency
    Scientists and engineers are developing more efficient cells
Solar cells have become world’s fastest growing way to produce electricity

## Slide 35: Using Solar Cells to Produce Electricity (4 of 5)
Notes: Figure 16.16 Solutions: A solar-cell panel provides electricity for lighting this hut in rural West Bengal, India. Critical thinking: Do you think your government should provide aid to poor countries for obtaining solar-cell systems? Explain.

## Slide 36: Using Solar Cells to Produce Electricity (5 of 5)
Notes: Figure 16.18 Using solar cells to produce electricity has advantages and disadvantages (Concept 16.3). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of using this technology outweigh its disadvantages? Why?

## Slide 37: 15.4 What Are the Advantages and Disadvantages of Using Wind Power? (1 of 2)
Wind is one of the fastest growing, least expensive, and cleanest ways to produce electricity
Wind is an indirect form of solar energy
  Uneven heating and earth’s rotation cause winds to blow
Kinetic energy captured by wind turbines
  Turbines grouped together in wind farms
    On land and at sea

## Slide 38: 15.4 What Are the Advantages and Disadvantages of Using Wind Power? (2 of 2)
Notes: Figure 16.20 Wind turbines convert the kinetic energy in wind to electricity, another form of kinetic energy (moving electrons). Wind power is an indirect form of solar energy.

## Slide 39: Using Wind to Produce Electricity (1 of 3)
Tall, long-blade turbines can extract more energy from the wind
Rapidly growing power source
  The United States, China, and Germany
Future is offshore wind farms
Wind power has potential to produce 40 times the world’s current electricity used

## Slide 40: Using Wind to Produce Electricity (2 of 3)
Wind is abundant, widely distributed, and inexhaustible
  Mostly carbon-free and pollution-free
High net energy yield
Largest potential areas are usually rural
  Smart grid needed to connect
Backup power source may be needed
  Alternative: large number of wind farms in different areas connected to smart grid

## Slide 41: Using Wind to Produce Electricity (3 of 3)
Notes: Figure 16.22 Using wind to produce electricity has advantages and disadvantages (Concept 16.4). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think the advantages outweigh the disadvantages? Why?

## Slide 42: 15.5 What Are the Advantages and Disadvantages of Geothermal Energy?
Geothermal energy can supply many areas with heat and electricity
  Generally low environmental impact
  Limited number of sites where it can be produced economically

## Slide 43: Tapping into the Earth’s Internal Heat (1 of 5)
Geothermal energy
  Heat stored in soil, underground rocks, and fluids in the earth’s mantle
Geothermal heat pump system
  Uses temperature difference between the earth’s surface and underground
  Fluid carried through a closed loop
  Can heat a building in winter and cool it in summer

## Slide 44: Tapping into the Earth’s Internal Heat (2 of 5)

## Slide 45: Tapping into the Earth’s Internal Heat (3 of 5)
Hydrothermal reservoirs
  Drill wells and extract dry steam, wet steam, or hot water
  The United States is the world’s largest producer
  Drilling geothermal wells is expensive
Geothermal is used exclusively in Iceland, and in 23 other countries

## Slide 46: Tapping into the Earth’s Internal Heat (4 of 5)
Notes: Figure 16.24 Power plants can produce electricity from heat extracted from underground geothermal reservoirs. The photo shows a geothermal power plant in Iceland that produces electricity and heats a nearby spa called the Blue Lagoon.

## Slide 47: Tapping into the Earth’s Internal Heat (5 of 5)
Notes: Figure 16.26 Using geothermal energy for space heating and for producing electricity or high-temperature heat for industrial processes has advantages and disadvantages. (Concept 16.5). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think the advantages of this energy resource outweigh its disadvantages? Why?

## Slide 48: 15.6 What Are the Advantages and Disadvantages of Using Biomass as an Energy Source?
Solid biomass
  Potentially renewable resource
  Requires large areas of land
  Exceeding replenishment rate produces a net gain in emissions of greenhouse gases
Liquid biofuels
  Can lessen dependence on oil
  Biofuel crops can degrade soil and biodiversity and increase emissions

## Slide 49: Producing Energy by Burning Solid Biomass (1 of 2)
Biomass
  Plant materials and agricultural waste that can be burned for fuel
Biomass plantations
  Fast growing trees and shrubs for repeated harvest
  Wood pellet production degrades forests
Burning wood and other forms of biomass produces CO2 and pollutants

## Slide 50: Producing Energy by Burning Solid Biomass (2 of 2)
Notes: Figure 16.27 Burning solid biomass as a fuel has advantages and disadvantages (Concept 16.6A). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think the advantages outweigh the disadvantages? Why?

## Slide 51: Using Liquid Biofuels to Power Vehicles (1 of 4)
Ethanol
  Ethyl alcohol produced from plants
Biodiesel
  Produced from vegetable oils
Advantages
  Crops can be grown throughout the world
  No net increase in CO2 emissions under certain circumstances
  Easy to store and transport

## Slide 52: Using Liquid Biofuels to Power Vehicles (2 of 4)
Brazil makes ethanol from sugarcane residue
  Medium net energy
2014: 43% of the corn produced in the United States was used to make ethanol
  Corn-based ethanol has a low net energy
  Producing and burning corn-based ethanol adds 20% more greenhouse gases than burning gasoline

## Slide 53: Using Liquid Biofuels to Power Vehicles (3 of 4)
Growing corn requires much water
Ethanol distilleries produce large volumes of wastewater
Cellulosic ethanol
  Alternative made of inedible cellulose
  Can be made from grasses that do not require fertilizer or replanting (perennials)
Algae can produce biofuel

## Slide 54: Using Liquid Biofuels to Power Vehicles (4 of 4)
Notes: Figure 16.28 Ethanol and biodiesel biofuels have advantages and disadvantages (Concept 16.6B). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why?

## Slide 55: 15.7 What Are the Advantages and Disadvantages of Using Hydropower?
Sources of hydropower
  Water flowing over dams
  Tidal flows
  Ocean waves
Downsides
  Environmental concerns
  Limited availability of suitable sites

## Slide 56: Producing Electricity from Falling and Flowing Water (1 of 2)
Hydropower
  Uses kinetic energy of moving water
  Indirect form of solar energy
  World’s leading renewable energy source
Top three producers
  China, Brazil, and the United States
Hydropower supplies half the electricity used on the West Coast

## Slide 57: Producing Electricity from Falling and Flowing Water (2 of 2)
Notes: Figure 16.30 Using large dams and reservoirs to produce electricity has advantages and disadvantages (Concept 16.7). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of this technology outweigh its disadvantages? Why?

## Slide 58: Using Tides and Waves to Produce Electricity
Produce electricity from flowing water
  Coastal bays and estuaries
Tidal energy dams
  France, Nova Scotia, and South Korea
Challenges
  Few suitable sites
  High costs
  Equipment damage from storms and saltwater corrosion

## Slide 59: 15.8 What are the Advantages and Disadvantages of Using Hydrogen as an Energy Source?
Hydrogen
  Simplest and most abundant chemical element
  Clean energy source
    Provided it is not produced with the use of fossil fuels
  Has a negative net energy
Fuel cells combine hydrogen and oxygen to produce electricity and water vapor

## Slide 60: Will Hydrogen Save Us? (1 of 4)
Advantages of hydrogen as a fuel
  Eliminates most outdoor air pollution from burning fossil fuels
  Would greatly slow climate change and ocean acidification

## Slide 61: Will Hydrogen Save Us? (2 of 4)
Some challenges
  Hydrogen chemically locked in water and organic compounds
  Negative net energy
    Serious limitation
  Fuel cells are costly
  CO2 emissions depend on method of hydrogen production

## Slide 62: Will Hydrogen Save Us? (3 of 4)
Notes: Figure 16.31 A fuel cell takes in hydrogen gas and separates the hydrogen atoms’ electrons from their protons. The electrons flow through wires to provide electricity, while the protons pass through a membrane and combine with oxygen gas to form water vapor. Note that this process is the reverse of electrolysis, the process of passing electricity through water to produce hydrogen fuel.

## Slide 63: Will Hydrogen Save Us? (4 of 4)
Notes: Figure 16.32 Using hydrogen as a fuel for vehicles and for providing heat and electricity has advantages and disadvantages. (Concept 16.8). Critical thinking: Which single advantage and which single disadvantage do you think are the most important? Why? Do you think that the advantages of hydrogen fuel outweigh its disadvantages? Why?

## Slide 64: 15.9 How Can We Make the Transition to a More Sustainable Energy Future?
We can make the transition to a more sustainable energy future by:
  Reducing waste
  Improving energy efficiency
  Using a mix of renewable energy resources
  Including the environmental and health costs of energy resources in their market prices

## Slide 65: Shifting to a New Energy Economy (1 of 2)
China and the United States
  Key players in making the shift to a new set of energy resources
  Each country uses about 20% of the world’s energy
Important actions to enable energy shift
  Use full-cost pricing
  Tax carbon emissions

## Slide 66: Shifting to a New Energy Economy (2 of 2)
Important actions (cont’d.)
  Decrease and eliminate government subsidies for fossil fuel industries
  Establish a national feed-in-tariff system
  Mandate that a certain percentage of electricity generated by utility companies be from renewable resources
  Increase government fuel efficiency standards

## Slide 67: Critical Concept: Environmental Change and Leadership
Environmental Leadership
  Lead by example
  Work within existing economic and political systems to bring about environmental improvement
  Buy sustainable products
  Run for local office

## Slide 68: What Can You Do?
Notes: Figure 16.33 Individuals matter: You can make a shift in your own life toward using energy more sustainably. Critical thinking: Which three of these measures do you think are the most important ones to take? Why? Which of these steps have you already taken and which do you plan to take?